## Slide 1: Master Device for TAVI Teleoperation Robot Master Thesis
Sensory-Motor systems Lab
Presenter: Armando Amorós
Supervisor: Dr. Robert Riener

## Slide 2: Transcatheter Aortic Valve Implantation/Replacement (TAVI)
Aortic artery
Calcified valve
Old valve displacement
New valve deployment
New valve
Images taken from https://www.maimonidesmed.org/heart-vascular-institute/centers/structural-heart-center/tavr
Notes: Aortic Artery
Left ventricle through the aortic valve
Fluoroscopy used during the whole intervention to track the catheter and wide wires

## Slide 3: Reduction of radiation illness and orthopedic injuries
Most common issues
https://www.fda.gov/radiation-emitting-products/medical-x-ray-imaging/fluoroscopy
https://www.infabcorp.com/product/revolution-full-overlap-lumbar-vest-skirt-703/
Fluoroscopy
Lead vest and skirt around 7 kgs
85% of brain tumors in interventionalists on the left side
50% have significant posterior subcapsular lens changes
60% have an incidence of spine issues after 21 years in practice
https://www.corindus.com/physician-resources
Notes: We come into the motivation of this master thesis which is
Subcapsular changes may lead to cataracts
33% miss work due to orthopedic issues
Early atherosclerosis in the carotid artery (Plaque builds inside the arteries)

## Slide 4: Teleoperation Benefits
17% Radiation reduction to the patient
95% Radiation reduction to the physicians
Robotic precision
Procedural Control
Input commands
Control feedback
Fluoroscopy Image
Control and sensing
Control and sensing
Visual guidance
Haptic feedback
Input commands
https://www.corindus.com/physician-resources

## Slide 5: Catheter Robotics Inc. – The Amigo remote control system
3 DOF
Endoscopy

## Slide 6: Stereoaxis - Niobe
Magnetic drive
Endoscopy
3D or 2D mouse

## Slide 7: Auris – Hansen Medical
3 DOF
Endoscopy
  Magellan
  Sensei
  Monarch

## Slide 8: Commercial Robots – CorPath GRX
2 DOF
Guide wire, catheter and stent balloon
One joystick per line
Made for PCI (Percutaneous coronary intervention)

## Slide 9: State of the Art Comparison Table
Company – Robot name | Catheter Type | Surgery type | Master device type
Catheter Robotics Inc. – The Amigo remote control system | At least 3 DOF, steerable catheter | Electrophysiology (EP), and radiofrequency catheter ablation of arrhythmias | Remote Controller
Stereoaxis – Niobe | At least 3 DOF, steerable catheter | Endocardial ablation, gastrointestinal endoscopy, and others. | Regular 2D or 3D mouse
Hansen Medical – Sensei X | At least 3 DOF, steerable catheter | Atrial Fibrillation (AF), and other arrhythmia procedures. | Combination of keyboard, and haptic device in delta robot configuration.
Auris – Monarch | At least 3 DOF, steerable catheter | Bronchoscopic visualization and access to patient airways for diagnostic and therapeutic procedures. | Videogame console type remote controller with buttons and joysticks.
Commercial Robots – CorPath GRX | 2 DOF catheters and guide wires. | Percutaneous coronary intervention (PCI) and Pulmonary vein isolation (PVI) | Joysticks

## Slide 10: Thesis objective
Find the most suitable master device for TAVI teleoperation
Notes: So, the objective of this thesis is to test between a variety of input devices and select the one that results more suitable for TAVI teleoperation

## Slide 11: Common Characteristics of all Devices
Manage 2 DOF (Degrees of freedom)
  1st DOF Axial movement
  2nd DOF Rotation movement
  No tip control
1st DOF
2nd DOF
Notes: Each one of the devices has to be able to control the catheter in the following way

## Slide 12: Keyboard Remote
1st DOF – Up and Down keys, Pressed Time* - Velocity
2nd DOF – Left and Right keys, Pressed Time* - Velocity
1st DOF – Up and Down buttons, Pressed Time* - Velocity (Push Buttons)
2nd DOF – Rotation disk, velocity to velocity mapping (Rotatory non contact sensor)
Notes: So know we are heading into th devices I chose to test, and how each one of them individually manage the 2 DOF
- Make remarks about analogic and digital

## Slide 13: Joystick Catheter like
1st DOF – Front and back rotation, distance to velocity (with potentiometer)
2nd DOF – Rotation over axis , distance to velocity (with potentiometer)
1st DOF – Push and pull motion , distance to velocity (with potentiometer)
2nd DOF – Rotation over axis , velocity to velocity (Rotatory non contact sensor)

## Slide 14: Advantages and Disadvantages
* Velocity of digital devices increases linearly over time with an initial offset
Sensor Type | Mapping | Device | Advantages | Disadvantages
Analogic | Position - Velocity | Joystick (Axial & Rotation) Catheter (Axial) | High Resolution with high control | No instant stop, prone to overshot Additional mechanics
 | Velocity - Velocity | Remote (Rotation) Catheter (Rotation) | Simplified mechanics Instant stop | Resolution highly dependent on sampling rate (Arduino) in combination with communication rate (Matlab)
Digital | Pressed Time* - Velocity | Keyboard (Axial & Rotation) Remote (Axial) | Simpler for first time users Instant stop when releasing the | Once released, it is necessary to build up velocity again No control in velocity
Notes: * Talk about the dead zone

## Slide 15: Experiments setup
Matlab sampling rate 30ms
Arduino process the velocities internally
Arduino sampling rate matched with Matlab for velocity – velocity devices
Serial communication
Analogic / Digital Signals
Velocity processing
Graphics process
Velocity request interruption
Send velocities

## Slide 16: Graphic Environment
2D representation of a catheter (simulation fluoroscopy image)
1st DOF (Axial movement) Up and Down
2nd DOF (Rotation movement) Left and Right
Green dot is the tip of the catheter
Catheter sinusoidal movement in rotation

## Slide 17: Experiment 1st DOF and 2nd DOF
Objective:
  Try to collocate the tip of the catheter (green square) inside the target (red square)
Metrics:
  RMSE in X and Y
Worlds (scenarios):
  3 different target trajectories per experiment
Repetitions:
  5 Times per world
  5 * 3Worlds *4Devices = 60Repetitions per experiment
  10 seconds each

## Slide 18: 1stDOF Experiment
Joystick is not significantly better than keyboard due to interaction P-Value = 0.006

## Slide 19: 1stDOF Learning/Training Curve

## Slide 20: 2ndDOF Experiment
Keyboard is significantly better than all other devices with P-Values < 4.50E-10

## Slide 21: 2ndDOF Learning/Training Curve

## Slide 22: Activation Error
Digital devices are significantly better than Joystick with P-Value around 0.01
Digital devices are significantly better than Catheter with P-Value around 0.001

## Slide 23: Experiment Maze
Objective:
  Navigate trough the maze until reaching the upper wall
  Reach the upper wall as fast as possible
  Avoid collisions with the walls and keep as much distance as possible
Metrics:
  Time
  Number of Collisions
  Dimensionless Squared Jerk
Worlds (scenarios):
  2 different mazes
Repetitions:
  5 Times per world
  5 * 2Worlds *4Devices = 40Repetitions per experiment
  No time limited
Notes: How important is DSJ

## Slide 24: Maze Experiment Time
There were no consistent significative differences between the devices due to interactions P-values < 0.05

## Slide 25: Maze Experiment Number of Collisions
Keyboard and Remote were significantly better than Joystick and Catheter with P-Values around 0.01
This results may be due overshoots in analogical devices

## Slide 26: Maze Experiment DSJ (Dimensionless Squared Jerk)
There were no consistent significative differences between the devices due to interactions P-values < 0.05

## Slide 27: Poll results

## Slide 28: Participants statistics and comments
Number of participants: 15
  Average age: 30.23
  % M: 46.15
  % F: 53.85
Most relevant comments
  Remote appears to be significantly slower than keyboard
  Takes some time to operate the joystick, but with time it feels the easiest to use
  Rotation in Joystick has too much dead zone and no low velocity
  (From Surgeon) Joystick as main device and Remote as detachable device

## Slide 29: Evaluation of the devices
Device | Delay/Latency | Friction | Reliability | Ergonomics
Keyboard | LOW | LOW | HIGH | MEDIUM The UP and DOWN arrows in the keypad are not spaced correctly for an appropriate one hand operation.
Remote | MEDIUM The used buttons have a pre-travel of 1.27, only activating at the end of the buttons total-travel. Giving the user the impression of non immediate action or delay, (actually reported in the polls by users). | LOW | HIGH | HIGH
Joystick | LOW | LOW | HIGH | HIGH
CatheterLike | LOW | HIGH Both, rotation and translation movements present friction, making the movements unstable at occasions. | MEDIUM The spring system intended to return automatically the catheter inside the dead zone on the 1st DOF is not working properly, making the catheter to keep moving even in resting position. | HIGH

## Slide 30: Conclusions
After the experiments and given the results in the:
  1st DOF Experiment
  Dimensionless squared jerk
  Training curves
  Poll results and comments
I consider the Joystick to be the most suitable option as a master device for the TAVI teleoperated robot

## Slide 31: Possible Following Steps
Explore mapping functions for analogic devices (other than linear)
Explore feedback strategies for a haptic device
Explore the possibility to have two master devices, adding a detachable secondary master device